## Slide 1
Designing of a Pitot-Static Tube
Team Members
Nipun Gunarathne – Device design Engineer
Wu Fan – Installation system design Engineering
Gaurawa Kovida – Test Engineer

## Slide 2
What is it really?
It is widely used to determine the airspeed of aircraft; the water speed of boats; and the flow velocity of liquids, air, and gases in industry
Introduction
Measures pressure difference () of stagnation pressure and static pressure and translates it into fluid flow velocity.
Since Bernoulli’s principles are considered here, fluid flow is treated as;
Non-viscous
Streamlined
Incompressible
No energy addition or loss
01

## Slide 3
The core physics of our setup relies on isolating dynamic pressure to calculate true airspeed.
A Pitot-static tube and the manometer connected simultaneously measures the stagnation pressure and the local static pressure.
•
: True Airspeed (m/s)
•
: Stagnation Pressure (Inner tube)
•
: Static Pressure (Outer PVC chamber)
•
: Air Density (~1.225 kg/m³)
Aerodynamic Theory: Bernoulli's Principle
v
https://forums.ni.com/t5/Example-Code/Pitot-Static-Tube-Pressure-Calculations-with-DAQmx-Acquisition/ta-p/3530828
02

## Slide 4
Initial Sketch
Prior to fabrication, the assembly was mapped out to ensure the geometry minimized turbulent wake over the measurement ports.
•
Forward Boom: 170mm length required to project past the scooter's frontal bow wave.
•
Outer Casing: 11mm PVC acts as the static pressure averaging chamber.
•
Inner Tube: 4mm rubber line routed directly from the tip to the sensor.
•
Mounting Angle: Designed with a 108° elbow to perfectly offset the scooter's steering stem rake.
Conceptual Design & Specifications
03

## Slide 5
Final Design & Specifications
04
Technical drawing done using
Autodesk Inventor

## Slide 6
Equipment & Materials
PCE-HVAC 2
Digital manometer
Electric conduit tube
Repurposed sauce bottle cap
Super glue
Epoxy
Glue gun and hot glue
Insulation tape
Silicon-rubber tube
05

## Slide 7
1. Modifying the Cap
The transparent sauce bottle cap featured sharp longitudinal edges.
These were sanded completely smooth to prevent tripping the boundary layer.
The cap was bonded flush to the 11mm PVC pipe using super glue, ensuring the 3mm stagnation tube protruded perfectly straight through the center.
2. The 108° Custom Elbow
Standard 90-degree PVC fittings would point the Pitot tube downward due to the scooter's raked stem.
We cut the pipes and bonded them using structural epoxy at exactly 100 degrees.
This ensures the forward boom remains perfectly horizontal and parallel to the incoming airflow during operation.
Fabrication: Nose Cone & Joints
06

## Slide 8
Assembly & Sealing
Creating the Static Chamber
For the system to work, the outer 11mm PVC pipe must act as a completely airtight pressure vessel. Any leaks would immediately equalize the pressure, destroying our data.
Two-part epoxy was pumped into the bottom exit gap, sealing the space around the 3mm inner tube. Once cured, all bonded joints were heavily wrapped in wiring tape to provide a secondary air seal and critical structural reinforcement against road vibrations.
07
Attachments reinforced through
Electrical insulation tapes

## Slide 9
Zip-Tie Implementation
For the initial proof-of-concept road tests, the Pitot-static assembly was mounted directly to the electric scooter's angled steering stem.
•
zip-ties were used to secure the vertical PVC stem.
•
This allowed for immediate field testing, easy height adjustment, and angle verification.
•
The digital manometer was secured near the handlebars for real-time memory logging.
•
The Trade-off: This non-rigid mounting solution introduced structural flex under high aerodynamic loads.
The Mount
08

## Slide 10
Testing was conducted on a flat, straight road. Speed was incrementally increased and held steady while logging values from the GPS Watch (Ground Speed) and the Manometer (Airspeed).
Test Phase | 01 | 02 | 03 | 04 | 05 | 06 | 07
Scooter Dash (Target) | 0 | 10 | 15 | 20 | 25 | 30 | 35
GPS Watch (km/h) | 0 | 11.89 | 16.00 | 21.10 | 25.79 | 32.29 | 35.59
Manometer (km/h) | 0 | 7.00 | 13.90 | 18.80 | 23.00 | 28.20 | 31.40
Data Collection
09
Track used for measurements

## Slide 11
Ground Speed vs. Measured Airspeed
10

## Slide 12
The "Bump" Effect
A slight lip where the sauce cap met the PVC created a minor speed bump for the air. This tripped the boundary layer, causing localized turbulence over the static holes and artificially lowering static pressure readings.
Misaligned Taps
Hand-drilling the 1mm static ports resulted in slight asymmetrical spacing. During steering wobbles or minor crosswinds, the static chamber could not perfectly average the pressure gradient around the circumference.
High-Speed Flex
At speeds exceeding 25 km/h, aerodynamic drag caused the zip-tie mount to flex backward. Tilting the nose cone off the direct stagnation axis immediately skewed the high-speed data.
Analysis: Identifying Deviations
11

## Slide 13
Theoretical CAD Model
The digital model represents perfect geometric symmetry, flush aerodynamic surfaces, and rigid 90-degree transitions without airflow disruption.
Physical Execution
The physical prototype highlights the realities of dorm-room fabrication: epoxy overflow, tape wrapping for vibration damping, and a repurposed nose cone.
Model vs. Final Build
12

## Slide 14
Conclusion & Future Scope
The DIY PVC Pitot-static tube successfully proved the concept, demonstrating a highly accurate measurement window near 20 km/h. To eliminate the aerodynamic deviations observed at high speeds, V2.0 will feature a fully 3D-printed uni-body design for perfect static port symmetry, coupled with a rigid, bolted aluminum clamp to completely eliminate mounting deflection.
13

## Slide 15
Thank you for your time.